## Slide 1
Packing a radio network into the fewest time slots
Distance-2 graph coloring, spatial reuse, and EMANE bridge
Athish M
Wireless protocol development take-home task
4×4 grid topology (9 slots)
Notes: Hi, I'm Athish. In this project, I took on the challenge of scheduling a wireless mesh network so that every radio gets to transmit without colliding with its neighbors, while keeping the overall frame as short as possible. The central trade-off is simple: fewer time slots in the frame means each radio gets to transmit more often, which maximizes throughput and minimizes latency. Over the next few minutes, I'll walk you through how I formulated this problem as a squared graph coloring problem, the five heuristics and two exact solvers I built, how I proved that 9 slots is the global optimum for the 4x4 benchmark grid, and how I verified the schedule both through an independent checker and through an offline EMANE emulation bridge.

## Slide 2
Why two radios can't talk at once
A and C can't hear each other, but both reach B, so their signals collide there.
d ≤ 500 m
d ≤ 500 m
out of range (d > 500 m)
A
Transmitter A
B
Shared receiver B (collision point)
C
Transmitter C
Radios 1 or 2 hops apart interfere and need different slots. Radios 3+ hops apart can share.
Notes: When two radios are within 500 meters of each other, they obviously can't transmit at the same time: that's direct distance-1 interference. But the real problem in multi-hop networks is the hidden terminal problem, which I've illustrated here. Radios A and C are more than 500 meters apart, so neither can hear the other. If A senses the channel, it thinks the air is clear. If C senses the channel, it thinks the same thing. However, both radios are within 500 meters of radio B in the middle. If A and C transmit in the same time slot, their signals arrive at B at the exact same moment, causing interference and packet corruption. This means any valid TDMA schedule must enforce a distance-2 rule: two radios that share a common neighbor can never share a timeslot. Radios separated by 3 or more hops, however, are far enough apart to safely reuse the same slot.

## Slide 3
My trick: square the graph
Coloring G² produces a conflict-free schedule: pairs 3+ hops apart stay unconnected so they can share a slot.
Physical graph G
1
2
3
4
5
Edges where distance ≤ 500 m
↓ Square it
Conflict graph G²
1
2
3
4
5
1-hop and 2-hop neighbours become adjacent
Nodes 1 and 4 are 3 hops apart: no edge connects them in G², so they reuse the same slot.
Notes: To solve this cleanly, I turned to graph squaring. The rule says no two nodes within 1 or 2 hops may share a slot. In graph theory, when you square a graph G to get G², an edge exists between two nodes if and only if their shortest-path distance in G is 1 or 2 hops. What this does is convert a complex multi-hop wireless problem into standard vertex coloring on G². Once you color G² so that adjacent vertices have different colors, every color represents a timeslot, and the schedule is mathematically guaranteed to be conflict-free. Notice the payoff: nodes separated by 3 or more hops, such as nodes 1 and 4 in this line, remain unconnected in G². That means they can safely reuse the same time slot, which is where our spatial reuse comes from.

## Slide 4
What I tried, in order
Method | Slots on 4×4 grid | Time
Greedy by degree (Welsh-Powell) | 9 | 0.06 ms
DSATUR (Saturation greedy) | 9 | 0.16 ms
Smallest-last (Degeneracy order) | 9 | 0.12 ms
1000 random restarts | 9 | 26.3 ms
Local search with Kempe swaps | 9 | 60.2 ms
Exact solver (CP-SAT) | 9 | 0.57 ms
All five reached 9, so I added an exact solver to find out whether 9 is the best possible.
Notes: I wanted to evaluate several coloring algorithms to see which one gave the tightest schedule. I started with greedy coloring ordered by degree, which took 0.06 milliseconds and found 9 slots. Then I tried DSATUR, which dynamically chooses the node with the most colored neighbors; that took 0.16 milliseconds and found 9 slots. Smallest-last ordering based on graph degeneracy took 0.12 milliseconds and gave the same 9 slots. To test whether random orders could shake loose an 8-slot schedule, I ran 1000 seeded random restarts; that took 26.3 milliseconds, but the best schedule remained 9 slots. Finally, I built a local search routine with Kempe-chain swaps and tabu search to try to eliminate the ninth color; after 60.2 milliseconds it still couldn't reach 8. Because all five heuristics stalled at 9, I couldn't tell if 9 was an algorithmic limitation or a physical lower bound. That's why I added an exact solver using Google OR-Tools CP-SAT with maximum-clique pre-coloring, solving in 0.57 milliseconds.

## Slide 5
The result on the 4x4 grid
$ python -m tdma.cli --coords-file grid_4x4_300m.json
Optimized Frame Length: 9 slots (Proven Optimum)
--------------------------------------------------
Node_01: Slot 8 Node_09: Slot 7
Node_02: Slot 4 Node_10: Slot 2
Node_03: Slot 5 Node_11: Slot 3
Node_04: Slot 8 Node_12: Slot 7
Node_05: Slot 6 Node_13: Slot 8
Node_06: Slot 0 Node_14: Slot 4
Node_07: Slot 1 Node_15: Slot 5
Node_08: Slot 6 Node_16: Slot 8
--------------------------------------------------
Slot 01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16
Slot 0 . . . . . 1 . . . . . . . . . .
Slot 1 . . . . . . 1 . . . . . . . . .
Slot 2 . . . . . . . . . 1 . . . . . .
Slot 3 . . . . . . . . . . 1 . . . . .
Slot 4 . 1 . . . . . . . . . . . 1 . .
Slot 5 . . 1 . . . . . . . . . . . 1 .
Slot 6 . . . . 1 . . 1 . . . . . . . .
Slot 7 . . . . . . . . 1 . . 1 . . . .
Slot 8 1 . . 1 . . . . . . . . 1 . . 1
13
14
15
16
09
10
11
12
05
06
07
08
01
02
03
04
Four corners share slot 8
Notes: Here is the actual schedule on the 4x4 grid topology. On the left is the real CLI output showing each node's timeslot. Node_01 is assigned Slot 8, Node_02 is assigned Slot 4, Node_03 is assigned Slot 5, Node_04 is assigned Slot 8, Node_05 is assigned Slot 6, Node_06 is assigned Slot 0, Node_07 is assigned Slot 1, Node_08 is assigned Slot 6, Node_09 is assigned Slot 7, Node_10 is assigned Slot 2, Node_11 is assigned Slot 3, Node_12 is assigned Slot 7, Node_13 is assigned Slot 8, Node_14 is assigned Slot 4, Node_15 is assigned Slot 5, and Node_16 is assigned Slot 8. On the right, notice the four corners: Node 1 at the bottom-left, Node 4 at the bottom-right, Node 13 at the top-left, and Node 16 at the top-right. All four are ringed in amber because they share slot 8. Because they are at least 3 hops apart in G, their signals do not interfere at any receiver, achieving spatial reuse.

## Slide 6
Why 9 is the best possible
9
slots is the mathematical floor
• Diagonal neighbors reach each other (424 m ≤ 500 m).
• Every pair in any 3×3 block is within 2 hops in G.
• That forms a 9-clique in G², forcing 9 distinct slots.
The brief's sample shows 5 slots with partial coordinates. Node_01 and Node_03 share slot 0, but both neighbor Node_02, so distance-2 forbids sharing.
13
14
15
16
09
10
11
12
05
06
07
08
01
02
03
04
Any 3×3 subgrid forms a 9-clique in G²
Notes: Could an even smarter algorithm find a schedule with fewer than 9 slots? The answer is no, and here is why. In this grid, nodes are spaced 300 meters apart horizontally and vertically. The diagonal distance between diagonal neighbors is 300 times the square root of 2, which is 424 meters. Since 424 meters is less than our 500-meter radio range, diagonal neighbors hear each other directly. Now take any 3x3 block of 9 radios, like the one highlighted in amber. Because diagonal radios are within 1 hop, every single pair of nodes in this 3x3 block is within at most 2 hops in G. Therefore, in the conflict graph G², every pair of these 9 nodes has an edge between them. That is a 9-clique. A clique of size 9 mathematically requires at least 9 distinct colors. So 9 slots is the absolute physical lower bound. Regarding the brief: its sample table showed 5 slots, but on this 300-meter grid, Node 1 and Node 3 cannot share a slot because Node 2 sits between them and would suffer a collision.

## Slide 7
Four topologies, same story
Chart: 
| 4x4 Grid | Sparse Line | Dense Cluster | Two Clusters
Exact Optimum | 9 | 3 | 16 | 8
Best Heuristic | 9 | 3 | 16 | 8
Topology | G edges | G² edges | Optimal
4x4 Grid | 42 | 90 | 9 slots
Sparse Line | 15 | 29 | 3 slots
Dense Cluster | 120 | 120 | 16 slots
Two Clusters | 56 | 56 | 8 slots
At 16 nodes plain greedy already finds the optimum, so the exact solver is how I know it.
Notes: I evaluated the optimizer across four benchmark topologies. For the 4x4 grid, we need 9 slots. For a 16-node linear chain spaced at 350 meters, the pattern repeats every 3 nodes, yielding 3 slots. For the dense cluster where all 16 nodes are within 500 meters of each other, G² forms a 16-clique, forcing every node into a distinct slot for 16 total. Finally, for two disconnected 8-node clusters separated by 3000 meters, both clusters run simultaneously, yielding 8 slots. In every case, the heuristics found the optimum on all four topologies. The value of having the exact solver isn't that the heuristics were failing, but that the exact solver provides proof that no better schedule exists.

## Slide 8
Part 2 and what's left
Optimizer
tested offline
JSON
tested offline
Bridge
tested offline
XML
tested offline
EMANE
not run
• EMANE needs pathloss set to ~500 m, or all 16 radios hear each other.
• Next step is running the container with virtual TAP interfaces.
• Future work covers joint time-frequency coloring and mobile nodes.
Notes: For Part 2, the goal was connecting the optimizer to EMANE's TDMA radio model. I built a bridge script that translates the JSON schedule into schema-compliant XML. The offline translation and NEM mapping are verified in automated tests. However, the live emulation inside a Linux container was not executed. If you run EMANE without calibrating pathloss, its radio model does not have our 500-meter cutoff: all 16 radios would hear each other across the multicast channel and collide. In a live testbed, you would publish LocationEvents or PathlossEvents so that signals drop off at 500 meters. Looking ahead, the next steps are running that container with live virtual interfaces, extending to 2D time-frequency coloring, and handling dynamic mobile topologies.